## Slide 1: Cristalografia
Professor: Paulo Moscon
Organização espacial de átomos e moléculas para compor materiais sólidos.

## Slide 2: Nuvem eletrônica de um único elétron

## Slide 7: Imagem real
STM image: Scanning tunneling microscope

## Slide 8: Imagem real

## Slide 9: Imagem real
Imagem obtida por Microscopia eletrônica de transmissão (MET)

## Slide 10: Materials and Packing
• atoms pack in periodic, 3D arrays
Crystalline materials...
-metals
-many ceramics
-some polymers
• atoms have no periodic packing
Noncrystalline materials...
-complex structures
-rapid cooling
crystalline SiO2
noncrystalline SiO2
"Amorphous" = Noncrystalline
Adapted from Fig. 3.23(b),
Callister & Rethwisch 8e.
Adapted from Fig. 3.23(a),
Callister & Rethwisch 8e.
Si
Oxygen
• typical of:
• occurs for:

## Slide 11: Energy and Packing
• Non dense, random packing
• Dense, ordered packing
Dense, ordered packed structures tend to have
lower energies.
Energy
r
typical neighbor
bond length
typical neighbor
bond energy
Energy
r
typical neighbor
bond length
typical neighbor
bond energy

## Slide 12: Ferramental matemático para estudar materiais sólidos
Um cristal é um arranjo periódico
As propriedades locais se repetem de com mesma periodicidade
Uma equação para localizar pontos equivalentes no espaço
Nota-se que apenas algumas geometrias de células unitárias são capazes de preencher o espaço sem deixar buracos

## Slide 13: Equação de base

## Slide 17: Geometrias que preenchem o espaço
1-Fold Rotation Axis - An object that requires rotation of a full 360o in order to restore it to its original appearance has no rotational symmetry. Since it repeats itself 1 time every 360o it is said to have a 1-fold axis of rotational symmetry. | 
2-fold Rotation Axis - If an object appears identical after a rotation of 180o, that is twice in a 360o rotation, then it is said to have a 2-fold rotation axis (360/180 = 2). Note that in these examples the axes we are referring to are imaginary lines that extend toward you perpendicular to the page or blackboard. A filled oval shape represents the point where the 2-fold rotation axis intersects the page. | 
3-Fold Rotation Axis- Objects that repeat themselves upon rotation of 120o are said to have a 3-fold axis of rotational symmetry (360/120 =3), and they will repeat 3 times in a 360o rotation. A filled triangle is used to symbolize the location of 3-fold rotation axis. | 
4-Fold Rotation Axis - If an object repeats itself after 90o of rotation, it will repeat 4 times in a 360o rotation, as illustrated previously. A filled square is used to symbolize the location of 4-fold axis of rotational symmetry. | 
6-Fold Rotation Axis - If rotation of 60o about an axis causes the object to repeat itself, then it has 6-fold axis of rotational symmetry (360/60=6). A filled hexagon is used as the symbol for a 6-fold rotation axis. | 

## Slide 18: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°

## Slide 19: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°
Base centered
monoclinic

## Slide 20: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°
Body centered
orthorhombic
Face centered
orthorhombic
Base centered
orthorhombic

## Slide 21: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°
Body centered
tetragonal

## Slide 22: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°
Simple cubic sc
Body centered cubic bcc
Face centered cubic fcc

## Slide 23: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°

## Slide 24: Lattice types
B3. Bravais lattices in 3D : 14
system | Number of lattices | Cell axes and angles
Triclinic | 1 | ¦a1¦≠¦a2¦≠¦a3¦ , α≠β≠γ
Monoclinic | 2 | ¦a1¦≠¦a2¦≠¦a3¦ , α=γ=90°≠β
Orthorhombic | 4 | ¦a1¦≠¦a2¦≠¦a3¦ , α=β=γ=90°
Tetragonal | 2 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=γ=90°
Cubic | 3 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ=90°
Trigonal | 1 | ¦a1¦=¦a2¦=¦a3¦ , α=β=γ<120°≠90°
Hexagonal | 1 | ¦a1¦=¦a2¦≠¦a3¦ , α=β=90° γ=120°

## Slide 25: Apenas paralelepípedos conseguem preencher o espaço
7 tipos simetrias de paralelepípedos foram classificadas com base nos três ângulos diretores e nos três comprimentos das arestas
Vértices, centros e centros das faces, são pontos de simetrias que quando considerados, aumentam de 7 para 28 os tipos de paralelepípedos
Destas 28 apenas 14 são verdadeiramente diferentes.

## Slide 26: Apenas paralelepípedos ? e a estrutura hexagonal?
•
•

## Slide 27: Existem apenas 14 arranjos cristalinos possíveis

## Slide 28: Modelo de esferas rígidas
Define-se uma célula que repetida no espaço, reproduz o sólido.

## Slide 29: Metais
Ligações não direcionais
A energia do sistema é mínima quando a distância entre os vizinhos é minimizada
A nuvem eletrônica Blinda o núcleo; tal como uma gaiola de Faraday
Como consequência disso, os metais tem as estruturas mais simples, geometricamente

## Slide 31
Exemplos
Cúbico de corpo centrado (CCC)
Body central cubic (BCC)
Cúbico de face centrada (CFC)
Face central cubic (FCC)
http://higheredbcs.wiley.com/legacy/college/callister/1118061608/vmse/xtalc.htm

## Slide 33: Fator de empacotamento atômico (FEA)